South Carolina Enterprise Information System

# Interface Operations Guide (IOG)

# IM386/SI001  - Sales Order Inbound Interface

Introduction

Document Purpose and Organization

The Interface Operations Guide (IOG) contains the interface specific information required for State of South Carolina Agencies to integrate with the SCEIS system. Each interface will contain a separate IOG with specific information. The IOG information will include the ADS number, description, file name(s), examples of load reports, frequency, run schedule, error conditions, etc. Additionally, the IOG will contain the file layout for the interface.

General system updates can be found on the SCEIS website, http://www.sceis.sc.gov

Sales Order Inbound Interface

| Interface ADS Number | IM386/SI001 |
| --- | --- |
| Inbound/Outbound | Inbound |
| Interface Title | Sales Order Interface |
| Interface Description | This is a batch interface for automatic Sales Order creation in SAP. Agencies will populate a standard file format (from either: legacy systems or manually prepared files) for all Sales Order Creation. The file will be imported into SAP and trigger the Sales Order Creation process within SAP. |
| Version | Version 2.0 |
| SCEIS Point of Contact |  |
| Source System | State Agency Subsystems |
| Destination System | SCEIS |
| Interface Type | Tab-delimited text file |
| Mode | Asynchronous |
| Frequency | The Agencies will transmit the interface files as needed. Files have the option of being processed upon receipt by SCEIS (at 30 to 45 minute intervals throughout the day) or being held and processed in a batch cycle at night. |
| File Name(s) | Inbound interface file: <bus. area>.<source system>.im386.salesorder.inbound.<date/time stamp> Example: f030.a1.im386.salesorder.inbound.20090706083021 Error file: <bus. area>.<source system>.im386.salesorder.errors.<original date/time stamp>.<creation date/time stamp> Example: f030.a1.im386.salesorder.errors.20090706083021.090706091512 |
| FTP Path | Determined by security requirements of the sending agency. |
| Manual Upload | Users with appropriate permissions will be able to upload properly formatted, tab-delimited text files to the interface for processing. The SAP transaction code for uploading a purchase order data file is ZIM386_SALES_UPLOAD. |

Version Control

| Version | Description of Change | Date |
| --- | --- | --- |
| 1.0 | Initial Version | 08/01/2009 |
| 2.0 | Update contact info | 03/13/2013 |

File Layout

| No. | Field Name | Req/ Opt | Type | Size | Format | Description |
| --- | --- | --- | --- | --- | --- | --- |
| ID Segment |  |  |  |  |  |
| 1 | Business Area | R | CHAR | 4 | XXXX | Agency Code - e.g. F030 |
| 2 | Source System Identifier | R | CHAR | 2 | XX | Agency specific Code to represent source system. Agencies discretion to use 2 unique characters as needed. |
| 3 | File Date | R | DATE | 8 | YYYYMMDD | File creation date - e.g. 20090531 |
| 4 | File Time | R | TIME | 6 | HHMMSS | File creation time in 24hr format - e.g. 183622 |
| 5 | Transaction Key | R | CHAR | 4 | XXXX | Identifies the type of SAP transaction – e.g. SD01 |
| 6 | Approval Status | R | CHAR | 1 | X | 1 = Agency approval Space = no Agency approval |
| 7 | Process | R | CHAR | 1 | X | 1 = Deferred Batch processing Space = Immediate processing |
| 8 | Approval Grouping | R | CHAR | 1 | X | N/A for this Interface |
| Header Segment |  |  |  |  |  |
| 9 | Header Sequence Number | R | NUMC | 4 | 9999 | Identifies the SAP documents in the interface file. All lines making up the first document in the file should have '0001' in this field; the lines for the second document should have '0002', etc. |
| 10 | PO Number (ORDER_HEADER_IN -PURCH_NO) | R | CHAR | 20 | X(20) | Work Order Number |
| 11 | Order Type (ORDER_HEADER_IN - DOC_TYPE) | R | CHAR | 4 | XXX | Always = ZOR |
| 12 | Sales Org (ORDER_HEADER_IN - SALES_ORG) | R | CHAR | 4 | XXXX | Always = ZDST |
| 13 | Distribution Channel (ORDER_HEADER_IN - DISTR_CHAN) | R | CHAR | 2 | XX | Always = Z1 |
| 14 | Division (ORDER_HEADER_IN - DIVISION) | R | CHAR | 2 | XX | Always = Z1 |
| 15 | Customer (ORDER_HEADER_IN - PARTN_NUMB) | R | NUMC | 10 | 9999999999 | Always = ????????? |
| Data Segment |  |  |  |  |  |
| 16 | Item Number (ORDER_ITEMS_IN -ITM_NUMBER) | R | NUMC | 6 | 999999 | Item Number on the Sales Order. Each Material Number is a separate Line Item Number |
| 17 | Delivery Plant (ORDER_ITEMS_IN -PLANT) | R | CHAR | 4 | XXXX | SAP Plant number where the Material or Service will be supplied from – e.g. IT03 – DSIT Sumter Street IT04 – DSIT Charleston |
| 18 | Required Delivery Date (ORDER_ITEMS_IN -REQ_DATE) | R | DATE | 8 | YYYYMMDD | Date that Material or Service is Required |
| 19 | Storage Location (ORDER_ITEMS_IN -STORE_LOC) | R | CHAR | 4 | XXXX | Always 0001 at this time |
| 20 | Billing Block (ORDER_ITEMS_IN -BILL_BLOCK) | R | CHAR | 2 | XX | Always = Z1 |
| 21 | Material Number (ORDER_ITEMS_IN -MATERIAL) | R | CHAR | 18 | X(18) | SAP Material Number |
| 22 | Quantity (ORDER_ITEMS_IN -TARGET_QTY) | R | NUMC | 14 | 9(10).999 | Quantity Requested (field is 14 digits including a decimal point and 3 decimal places) |
| 23 | Work Order Text (ORDER_HEADER_IN -HEADER_ NOTE_1) | O | CHAR | 2500 | X(2500) | Any Additional Text for the Work Order. Only passed in first Item Number record in the Sales Order, otherwise will be null. |

Note: Every record on the input file contains all data fields. The ID and Header segment fields are repeated on every record.

Process Flowchart

Miscellaneous Processing Notes

- The file format is a TAB-delimited text file.

- All records within the file have three parts.

  - ID Segment contains systems information to specify how the file will be processed.  It also contains information to uniquely identify a transaction by the source system that created it.  Important: The data in the ID Segment should be the same for every record on the file.

  - HEADER Segment has the header level information for the SCEIS transaction.

  - DATA Segment contains the line item information for the SCEIS transaction.

- Each file sent for processing will be uniquely identified by the combination of Business Area, Source System ID, File Date and File Time.  Each combination of this data will be logged by the system and any subsequent files sent with same combination will be rejected as duplicates.

- Agency contact email addresses will need to be provided to SCEIS for each agency / subsystem that will use the interface. This information will be requested as part of a testing and acceptance process for each agency system.  Transmittal controls, Valid / Error reports, etc will be emailed to these designated users as files are processed by the interface. In the examples below, notifications for system “A1” would be emailed to Joe and Mary; Tom would the get emails for the “B1” system.

Agency	System	Email

F030		A1		joe@agency.gov

F030		A1		mary@agency.gov

F030		B1		tom@agency.gov

General FTP Processing Notes

The preferred method of data transfer will be via secure FTP, and SCEIS will host an FTPS server for this purpose.

There will be a folder structure set up on the server for each business area. Sub-folders will be created if necessary based on the security requirements of the sending agency. Security will be set up appropriately on the folders so that users will only have access to their data.

In the example below there are separate AR and AP interface folders for business area E120. On the other hand for E160, all interfaces would use the same FTP folder - “/e160”.

/f030

/sd

/ar

/ap

/vendor

/e160

/e200

/fi

/mm

To send files to SCEIS‐inbound or receive files from SCEIS‐outbound interfaces, FTPS client software will be used on the agency side.  Example FTP connection options are shown in the following print screen. (Using the CoreFTP desktop client software – in other clients, the options may be slightly different.)

For further questions/concerns regarding the File Transfer Protocol procedures. Please contact the SCEIS Interface Team at interfaces@sceis.sc.gov